## Slide 1
Interdiction And Restoration Of Interdependent Infrastructure Systems
in Military Operations
Liqun Lu, Zhaodong Wang, Dr. Yanfeng Ouyang
Nov. 15th, 2016
INFORMS 2016 Annual Meeting
I L L I N O I S

## Slide 2: Outline
Background
Methodology
  Infrastructure interdependency model
  Interdiction and restoration optimization
  Solution Algorithm
  Cutting plane algorithm
  Two-stage genetic algorithm
Case Study
Conclusion

## Slide 3: Military Doctrine
Landpower is the ability—by threat, force, or occupation—to gain, sustain, and exploit control over land, resources, and people.
Landpower includes the ability to—
  Impose the Nation’s will on an enemy, by force if necessary.
  Engage to influence, shape, prevent, and deter in an operational environment.
  Establish and maintain a stable environment that sets the conditions for political and economic development.
  Address the consequences of catastrophic events—both natural and man-made—to restore infrastructure and reestablish basic civil services.
  Support and provide a base from which joint forces can influence and dominate the air and maritime domains of an operational environment.
(Dr. Steve Hart, USMA)
Notes: First off, here is a slide from a West Point professor, about the military operation doctrine. It talks about the concept of landpower, which is the ability to gain, sustain, and exploit control over land, resources, and people. I want to emphasize some of its components. Those are, the ability to…

## Slide 4: Military Operation Art
Break it bad
Fix it Fast
SMART
(Dr. Steve Hart, USMA)
Notes: Coming to practice from the philosophy, this figure shows offense military operation plan phases versus level of effort. In Phase II and III, the military needs to seize initiative by destroying some of the enemy’s infrastructures and then dominate the enemy’s territory, we call it break it bad. After the offense military takes control over the region, it now needs to stabilize its control by rebuilding the damaged infrastructure system so as to provide sufficient resources to the civilians. This task is call fix it fast. However, in the past military operations, the interdiction of infrastructure did not take account of the cost of future recovery in phase IV. For example, a bridge carrying multiple oil and gas pipelines in northern Iraq was destroyed by U.S. army during the conflict. After the combat period the U.S. military decided to repair this bridge, and planed to finish the project within two months and with 5 million dollars. But due to unexpected difficulty it was prolonged to a three year project costing over 100 million dollars. Throughout Iraq, more than 15 billion dollars was spent merely to repair the damaged infrastructure system. Therefore, instead of break it bad, we really need to break it smart. That means we need to plan the course of actions considering both effectiveness and cost-efficiency.

## Slide 5: Objective
Q2
Q1
Demonstration of
military landpower
Phase II&III:
maximize the interdiction impact
Phase IV :
maximize the restoration benefit
Evaluation of military operations
Optimization of course of actions
Notes: The demonstration of military landpower includes both maximizing the interdiction impact during phase II and phase III and maximizing the restoration benefit during phase IV. To achieve these goals, we have to answer two questions directly. First how do we evaluate the effectiveness of interdiction/restoration actions in the interdependent infrastructure network with complex population behavior? Second is how do we optimize over the course of actions. We answer the first question using an interdependent infrastructure network model, and solve the second using a two-stage optimization framework.

## Slide 6: Interdependency Model
System disruption propagation
Population behavior
Infrastructural
interdependency model
Input: interdiction/restoration
Output: infrastructure status and society well-being
Lu et al. (submitted 2016)
Notes: The interdependency model was first introduced in a soon-to-be-published work. It takes input of interdiction and restoration actions and considers the mutual impact between system disruption propagation and population behavior. The output of the model is the infrastructure status and society well-being in terms of resource accessibility. The model essentially is a network equilibrium where population may compete with facilities to obtain resources.

## Slide 7: Failure Propagation Mechanism
Support Type | Realization | Example | Reason of failure | Failure
Functional Support (strong support) | Direct physical infrastructural links | Power cable Water pipeline … | Failure of any one of the support facilities | Support failure
Resource Support (weak support) | Commodity flow | Fuel delivered by transportation | Unsatisfied resource demand | Resource failure
Notes: To elaborate, we consider two types of infrastructure interdependencies, functional support and resource support. The functional support are realized by direct physical links such as power cable and water pipeline. The failure of any of the support facilities will lead to certain failure of the supported facilities. We call such failure support failure. Resource support is usually realized by commodity flow, such as fuel supply delivered to gas station by transportation. Unsatisfied resource demand leads to failure of facilities. Which are called resource failure.

## Slide 8: Failure Propagation Mechanism
Diesel tank
Diesel generator
Water pump
Functional Support
Resource support
(a)
(b)
(c)
(d)
(e)
Example
(a)→(b): Initial disruption at diesel tank
(b)→(c): Resource failure at generator
(c)→(d): Support failure at pump
(b)→(e): Diesel generator seeks supply from another diesel tank
Notes: This graph shows an example of support failure and resource failure. The water pump is supported by the diesel generator via functional support, and the generator supported by the diesel tank via resource support. When the tank is disrupted, it may happen that the generator could not get sufficient supply from the other tanks due to limited resource capacity or high transportation cost, which is resource failure. In such case the water pump will also fail due to support failure. In another scenario, if the generator can get sufficient fuel supply from the other tank, the failure at the original tank will not propagate.

## Slide 9
Interdependency Model Formulation
Interdependency function
Functional support
Resource support
Initial disruption
Finite resource capacity
Flow conservation
(1)
(2)
(3)
Restoration
(4)
System equilibrium
(5)
(6)
(7)
(8)
Definition If there exists such that, then describes an equilibrium in the network, where is defined by the above constraints.
9
Non-negativity
Resource capacity constraint
Notes: As we mentioned, the model is essentially a network equilibrium where the facilities and population are network users. These formulations describe the model and we do not intend to go into details here.

## Slide 10: Interdiction and Restoration
Interdiction stage
Restoration stage
failed
functioning
Notes: Let’s then look at the interdiction-restoration problem in a graphical way. Each of these nodes represents a facility. Color green means the facility is functioning and red means failed. In the interdiction stage, we select some facilities as targets to interdict. The failure of these facilities will propagate in the infrastructure system due to interdependency. Then among all the disrupted facilities in the disruption aftermath, we select some of them to repair. With these facilities working, some others will also be functioning again.

## Slide 11: Interdiction and Restoration
Stage | Decisions | Objective
Interdiction | Select facilities to interdict in the intact system | Maximize impact
Recovery | Select facilities to restore among the failed ones | Maximize restored social function
Objective
Budget constraint
Social welfare constraint
1st stage objective
2nd stage objective
Notes: In the interdiction stage, the objective is to maximize the interdiction impact, and in the recovery stage, it is to maximize the restored social function. We put different weights to these two objectives and add them up as our final objective. There is a budget constraint for military operations. Moreover, we need to restore the final state social function to a certain level such that the basic need of population can be satisfied.

## Slide 12: Solution Algorithm
Cutting Plane Algorithm
Implemented to solve for interdependency model equilibrium
Two-Stage GA
Solve the two-stage optimization
Based on Nguyen and Dupuis (1984)
Evaluate 1st stage decision based on the optimal 2nd stage decision
Notes: We use a cutting plane algorithm to solve the system equilibrium for the interdependency model. This algorithm was based on the work of Nguyen and Dupuis in 1984. We will also skip the details. Then we use a two stage GA to solve the optimization.

## Slide 13: Case Study
City: Maiduguri, Nigeria
  Total population of 1.2 million
  Occasional natural disasters: flood, draught, etc.
  Military events and terrorist attacks
  Model setting
  Seven layers of infrastructure networks and a community layer
  20*20 grid transportation network
  Uniform interdiction cost
  Use three levels of restoration cost: low/moderate/high
Notes: … We select this city for case study because it is a mid-size city suitable for research practice.

## Slide 14: Case Study

## Slide 15: Case Study
Notes: Power transmission – substation
Proxy transformers – triangles
Power generators – squares

## Slide 16: Case Study

## Slide 17: Case Study
Notes: Water treatment plant – big circles - support by power substation
Water tanks (triangles, resource support) / towers (small circle, functional support)
Water vendors (squares)

## Slide 18: Case Study
Notes: Institutions
4 hospitals (power supply from transformers and water supply via resource support from all available water facilities)

## Slide 19: Case Study
Notes: Three food processing factories, several food markets. Independent on other systems.

## Slide 20: Case Study
Scenario 0: moderate budget
Interdiction decision
  power transmission
  fuel depot
Interdiction aftermath
  entire power grid
  fuel system
  water system
  hospitals
Impact on population
  0% access to water
  0% access to healthcare
  100% access to food
Notes: Scenario 0 is our benchmark case, where we have a moderate budget, such that we cannot afford to repair high restoration cost facilities such as fuel depot and power substation.

## Slide 21: Case Study
Scenario 0: moderate budget
Restoration decision
  power transmission
  too costly to restore fuel depot: only recover one fuel tank
Restoration effectiveness
  entire power grid
  sufficient fuel supply
  water vendors
  hospitals
Impact on population
  90% access to water
  95% access to healthcare
  92% access to food

## Slide 22: Case Study
Scenario 1: low budget
Interdiction decision
  fuel depot
Interdiction aftermath
  fuel system
  water vendors
  hospitals
Impact on population
  52% access to water
  4% access to healthcare
  89% access to food

## Slide 23: Case Study
Scenario 1: low budget
Restoration decision
  2 fuel tanks
Restoration effectiveness
  sufficient fuel supply
  water vendors
  hospitals
Impact on population
  90% access to water
  96% access to healthcare
  93% access to food

## Slide 24: Case Study
Scenario 2: high budget
Interdiction decision
  power transmission
  fuel depot
  3 food processing factories
Interdiction aftermath
  power grid
  fuel system
  water system
  hospitals
  food system
Impact on population
  0% access to water
  0% access to healthcare
  0% access to food

## Slide 25: Case Study
Scenario 2: high budget
Restoration decision
  power transmission
  fuel depot
  3 food processing factories
Restoration effectiveness
  all system back to functioning
Impact on population
  100% access to water
  100% access to healthcare
  100% access to food

## Slide 26: Case Study
Scenario 3: moderate budget, no final state constraint and only consider first stage objective (terrorist attack)
Interdiction decision
  power transmission
  fuel depot
  2 food processing factories
Interdiction aftermath
  power grid
  fuel system
  water system
  hospitals
  food system
Impact on population
  0% access to water
  0% access to healthcare
  5% access to food

## Slide 27: Conclusion and Future Work
  This study investigates the problem where a military force needs to help rebuild the damaged infrastructure system after its interdiction
  The problem is modeled as a two-stage optimization, solved using GA
  Interdiction/restoration actions are evaluated using an infrastructure interdependency model, solved in an embedded cutting plane algorithm
  Case study on theoretical war-game scenarios reveals interesting results

## Slide 28: Thank you!