## Slide 1: Vulnerability of Interdependent Urban Infrastructure Networks: Failure Propagation and Societal Impacts
Liqun Lu1, Xin Wang2, Yanfeng Ouyang1, Natalie Myers3, Jeanne Roningen3, George Calfas3
[1. Department of Civil and Environmental Engineering, University of Illinois at Urbana-Champaign; 2. Department of Industrial and Systems Engineering, University of Wisconsin-Madison; 3. Construction Engineering Research Laboratory, US Army Engineer Research and Development Center]
Abstract
Modern cities relies heavily on interdependent infrastructure systems
Disruptions often propagate within and across physical infrastructure networks and result in catastrophic consequences.
The reaction of population communities to disruptions may further transfer and aggravate the burden on surviving infrastructures
A game-theoretical equilibrium model is developed to investigate the mutual influence between the infrastructures and the communities
  Multi-layer infrastructure network
  Two types of infrastructure failure patterns
  Network equilibrium is extended to address redistribution of resource demand
Societal impact is estimated based on communities’ resource demand loss, cost increase, and total infrastructure failure
A real-world case study on Maiduguri, Nigeria, is implemented to demonstrate the model and reveal insights
Background
Modern urban infrastructure systems
  Multiple networked systems
  Jointly functioning
  High interdependency
  Vulnerability to disruptions
  Urban population
  Great amount & density
  Highly dependent on infrastructural system
  Population behavior will be reshaped by disruptions
  System disruptions
  Natural disasters or human-induced actions
  System cascading failure
  Reduce system performance
  Insufficient resource for population
Objectives
Methods
Results
Conclusions
A holistic mathematical model is proposed to evaluate the vulnerability of an urban infrastructure system against the threats of cascading failures
  The infrastructure systems are modeled as a multi-layered network, where each functioning infrastructure unit is modeled as a node
  Two types of infrastructure failure mechanisms are modeled to estimate the cascading failure
  A network equilibrium model incorporating queueing and congestion is formulated, and mathematical proofs for equilibrium existence and uniqueness is shown
  A diagonalization algorithm is developed to solve the equilibrium and to compute societal impacts, with the discussion on the convergence of the algorithm
  Through a case study on Maiduguri, many interesting insights are observed
  A system with greater resource capacity is more resilient to disruptions
  Disruption happening at some “seemingly” critical infrastructures may not severely affect the entire system
  Maintaining the functionality of some infrastructures may not benefit the society
…
Transportation
Power
Water
Community
System disruption propagation
Understand infrastructural interdependencies
Model cascading failure
Impact on population
Estimate population’s demand on resources
Predict people’s resource-access behavior
Resource-providing facilities disrupted
Commodity flow based on population reaction
Generalize various types of interdependencies among infrastructures
Estimate entangled system failure and equilibrium community behavior
Evaluate the cascading propagation of disruptions and the consequential societal impacts
Support Type | Realization | Example | Reason of failure | Failure
Functional Support | Direct physical infrastructural links | Power cable Water pipeline … | Failure of any one of the support facilities | Support failure
Resource Support | Commodity flow | Fuel delivered via transportation | Resource access cost becomes too high | Resource failure
Infrastructural interdependency categorization
Facility/Community resource accessing behavior
  Resource users travel through transportation network to acquire resource
  The cost of traversing each transportation link increases with flow
  Limited resource supply also increases the difficulty for resource procurement
  The demand decreases with procurement cost
  Augmented network representation
  The problem can be converted into an equivalent Wardrop equilibrium problem with link interactions
Problem formulation
Interdependency function
Functional support
Resource support
Initial disruption
Finite resource capacity
Nash equilibrium
System equilibrium
(1)
(2)
(3)
(4)
(5)
(6)
(7)
(8)
(9)
(10)
(11)
(12)
Equilibrium analysis and solution approach
Proposition 1. There exists a unique equilibrium if:
(1) the interdependency function is continuous, concave, and non-decreasing, and
(2) the demand-loss penalty is monotonically increasing.
Proposition 2. The diagonalization method gives the unique equilibrium point with guaranteed global convergence if either one of the following two conditions is satisfied:
i) The facility status is not sensitive to resource failure;
ii) The resource demand is inelastic enough, such that the demand-loss penalty is highly sensitive to the lost demand
  City: Maiduguri, Nigeria
  Total population of 1.2 million
  Occasional natural disasters: flood, draught, etc.
  Overwhelming number of internally displaced persons (IDPs)
  Military events and terrorist attacks threaten the people and infrastructure
  Model setting
  Seven layers of infrastructure networks and a community layer
  Six categories of communities
  Case Study
  Disruption at the power substation
Different scenarios | Food |  |  | Water |  | 
 | Access cost increment | Population lost resource | Failed facilities (total 11) | Access cost increment | Population lost resource | Failed facilities (total 28)
0: Case Study | -7% | 0.0% | 0.0 | 458% | 4.3% | 17.5
1: No Queueing Cost | -36% | 0.0% | 0.0 | 0.5% | 0.0% | 18.0
2: Moderate resource cap. | -49% | 0.0% | 0.0 | -25% | 0.0% | 17.5
3: High resource cap. | -54% | 0.0% | 0.0 | -35% | 0.0% | 17.5
4: Init. Water | -27% | 0.0% | 0.0 | 20% | 2.9% | 9.3
5: Init. Fuel | 22% | 1.3% | 0.5 | 157% | 5.9% | 10.6
6: Water and Fuel | -2% | 0.0% | 0.3 | 860% | 8.7% | 16.2
  Result summary
  Failed facilities:
  water: 17.5/28
  food: 0.0/11
  education: 84.0/84
  healthcare: 4.0/4